## Slide 1: Embedded Linux
Anatomy of a Linux-based System
Notes: Hello and welcome to the Linux for Embedded Systems lecture. This is the third lecture of the course.

## Slide 2: Goals
To provide a more detailed view of the Linux architecture
To illustrate the device tree details
To introduce the U-BOOT bootloader
Notes: The aim of this lecture is to
  - Provide a more detailed overview of the Linux architecture.
  - Illustrate the device tree details.
  - Introduce the U-Boot bootloader.

## Slide 3: Summary
Linux architecture
Device trees
The U-BOOT bootloader
Notes: We will start with a more in-depth look at the Linux architecture.

## Slide 4: Summary
Linux architecture
Device trees
The U-BOOT bootloader
Notes: We will start with a more in-depth look at the Linux architecture.

## Slide 5: Linux Architecture
Layered architecture based on two levels:
  User space
  Kernel space
User space and kernel space are independent and isolated
User space and kernel space communicate through special purpose functions known as system calls
GNU C Library (glibc)
System Call Interface
Kernel
Board Support Package (BSP)
Application
System Programs
User Space
Kernel Space
Notes: The Linux architecture is layered and based on two main levels: user space and kernel space. These two spaces are independent of one another and isolated. They are able to communicate with one another through special-purpose functions known as system calls.

## Slide 6: Linux Architecture
Application
  Software implementing the functionalities to be delivered to the embedded system user
System programs
  User-friendly utilities to access operating system services
GNU C Library (glibc)
  Interface between the User Space and the Kernel Space
GNU C Library (glibc)
System Call Interface
Kernel
Board Support Package (BSP)
Application
System Programs
User Space
Kernel Space
Notes: Taking a more detailed look at the user space, this diagram illustrates three main components. The first component of user space is the application. This is software that implements the functionalities to be delivered to the embedded system user.
The second component is system programs. These are user-friendly utilities that enable access to operating system services.
The final component is the GNU C Library or glibc, which acts as an interface between user space and the kernel space.

## Slide 7: Linux Architecture
System call interface
  Entry points to access the services provided by the Kernel (process management, memory management)
Kernel
  Architecture-independent operating system code
  It implements the hardware-agnostic services of the operating system (e.g. the process scheduler).
Board Support Package (BSP)
  Architecure-dependant operating system code
  It implements the hardware specific services of the operating system (e.g. the context switch).
GNU C Library (glibc)
System Call Interface
Kernel
Board Support Package (BSP)
Application
System Programs
User Space
Kernel Space
Notes: We can then look at the three main components of the kernel space. The first being the system call interface. This provides entry points to access the services provided by the kernel, such as process management and memory management.
Then, there is the actual kernel itself. This is architecture-independent operating system code. It implements the hardware-agnostic services of the operating system, such as the process scheduler.
Finally, there is the board support package or BSP, which is architecture-dependent operating system code. This implements hardware-specific services of the operating system, such as context switches.

## Slide 8: Conceptual View of the Kernel
The Kernel can be divided in five subsystems:
  Process scheduler
  Memory manager
  Virtual file system
  Inter-process communication
  Network
Most of them are composed of:
  Hardware-independent code
  Hardware-dependent code
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: Let’s take a deeper look at the kernel and its different parts.
The kernel can be divided into five subsystems. These are the process scheduler, memory manager, virtual file system, inter-process communication (IPC), and the network.
Most of them are made up of both hardware-independent and hardware-dependent code.

## Slide 9: Process Scheduler
Main functions:
  Allows processes to create new copies of themselves
  Implements CPU scheduling policy and context switch
  Receives, interrupts, and routes them to the appropriate Kernel subsystem
  Sends signals to user processes
  Manages the hardware timer
  Cleans up process resources when a processes finishes executing
  Provides support for loadable Kernel modules
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware Driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: First, we will take a look at the process scheduler. Simply put, a process scheduler is responsible for the decision making of which processes are running at what time. This is achieved with the help of a variety of functions.
The main functions are as follows:
  - Processes can create new copies of themselves.
  - Implements CPU scheduling policy and context switch
  - Receives interrupts and routes them to the appropriate kernel subsystem
  - Sends signals to user processes
  - Manages the hardware timer
  - Cleans up process resources when a process finishes execution
  - Provides support for loadable kernel modules

## Slide 10: Process Scheduler
External interface:
  System calls interface towards the user space (e.g. fork())
  Intra-Kernel interface towards the kernel space (e.g. create_module() )
Scheduler tick:
  Directly from system calls (e.g. sleep())
  Indirectly after every system call
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware Driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The System calls interface faces towards the user space, such as the fork method. While the intra-kernel interface faces towards the kernel space, such as the create module method.
The scheduler is called directly from system calls such as sleep. It is called indirectly after every system call.

## Slide 11: Process Scheduler
Interrupts:
  Fast interrupt requests (FIQ) can be generated for events that need to be handled as they occur.
  Standard interrupt requests (IRQ) can be generated for more general interrupt events.
  As such – FIQs have a higher priority.
    FIQs can interrupt code servicing an IRQ, but not vice versa
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware Driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: Fast interrupt requests (FIQ) can be generated for events that need to be handled as they occur – this can include things such as keyboard or mice input. Standard interrupt requests (IRQ) can be generated for more general and common interrupt events. As such, FIQs have a higher priority – this means that they can interrupt code servicing an IRQ, but not vice versa.

## Slide 12: Memory Manager
It is responsible for handling:
  Large address space: user processes can reference more RAM memory than what exists physically
  Protection: the memory for a process is private and cannot be read or modified by another process; also, the memory manager prevents processes from overwriting code and read-only-data.
  Memory mapping: processes can map a file into an area of virtual memory and access the file as memory.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The next component we will look at is the memory manager. This component is responsible for handling a variety of tasks. The first is the ability to sort and manage a large address space. This means that user processes can reference more RAM than what exists physically.
Another task for the memory manager is memory protection. The memory for a process is private and should not be read or modified by another process. Also, the memory manager prevents processes from overwriting code and read-only data.
This component is also responsible for memory mapping. A process can map a file into an area of virtual memory and then access the file as memory.

## Slide 13: Memory Manager
It is responsible for handling:
  Fair access to physical memory: it ensures that processes all have fair access to the memory resources, ensuring reasonable system performance.
  Shared memory: it allows processes to share some portion of their memory (e.g. executable code is usually shared amongst processes).
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: Another of its responsibilities is to allow fair access to physical memory. It is required to ensure that processes all have fair access to the memory resource, while also ensuring reasonable system performance.
Finally, it is responsible for managing shared memory. It needs to allow processes to share some portion of their memory if required. For example, executable code is usually shared amongst processes.

## Slide 14: Memory Manager
It uses the Memory Management Unit (MMU) to map virtual addresses to physical addresses.
  It is conventional for a Linux system to have a form of MMU support.
Advantages:
  Processes can be moved among physical memory maintaining the same virtual addresses.
  The same physical memory may be shared among different processes.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The component makes use of the memory management unit (MMU) to map virtual addresses to physical addresses. It is conventional for a Linux system to have a form of MMU support.
The advantages of this are that processes can be moved about in physical memory, while maintaining the same virtual address. Also, the physical memory may be shared among different processes.

## Slide 15: Memory Manager
It swaps process memory out to a paging file when it is not in use:
  Processes using more memory than physically available can be executed.
The kswapd Kernel-space process (also known as daemon) is used for this purpose.
  It checks if there are any physical memory pages that haven’t been referenced recently .
  These pages are evicted from physical memory and stored in a paging file.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The memory manager swaps process memory out to a paging file while it is not in use. Due to this, processes using more memory than physically available can be executed.
The kswapd (“k swap d”) kernel-space process or daemon is used for this purpose. It checks if there are any physical memory pages that haven’t been referenced recently. These pages are evicted from physical memory and stored in a paging file.

## Slide 16: Memory Manager
The MMU detects when a user process accesses a memory address that is not currently mapped to a physical memory location.
The MMU notifies the Linux Kernel the event known as page fault.
The memory manager subsystem resolves the page fault.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The MMU detects when a user process accesses a memory address that is not currently mapped to a physical memory location. The MMU notifies the Linux kernel of the event, known as a page fault. The memory manager subsystem will then resolve the page fault.

## Slide 17: Memory Manager
If the page is currently swapped out to the paging file, it is swapped back in.
If the memory manager detects an invalid memory access, it notifies the event to the user process with a signal.
If the process doesn’t handle this signal, it is terminated.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: If the page is currently swapped out to the paging file, it is swapped back in. If the memory manager detects an invalid memory access, it notifies the event to the user process with a signal. If the process doesn’t handle this signal, it is terminated.

## Slide 18: Memory Manager External Interfaces
System call interface:
  malloc()/free(): allocate or free a region of memory for the process's use
  mmap()/munmap()/msync()/mremap(): map files into virtual memory regions
  mprotect(): change the protection on a region of virtual memory
  mlock()/mlockall()/munlock()/munlockall(): super-user routines to prevent memory being swapped
  swapon()/swapoff(): super-user routines to add and remove swap files for the system
Intra-Kernel interface:
  kmalloc()/kfree(): allocate and free memory for use by the kernel’s data structures
  verify_area(): verify that a region of user memory is mapped with required permissions
  get_free_page()/free_page(): allocate and free physical memory pages
Notes: There are a bunch of methods for interfacing with the memory manager.
For the system call interface, there is
  - “malloc” or “free”, which allocates or frees a region of memory for the process to use.
  - “mmap”, “munmap”, “msync”, or “mremap”, which maps files into regions in virtual memory.
  - “mprotect”, which changes the protection on a region of virtual memory
  - “mlock”, “mlockall”, “munlock”, or “munlockall”, which are super user routines to prevent memory being swapped
  - “swapon” or “swapoff”, which are super user routines to add and remove swap files for the system

## Slide 19: Memory Manager Architecture
Main components:
  System call interface: it provides memory manager services to the user space.
  Memory mapped files: it implements memory file mapping algorithms.
  Core memory manager: it is responsible for implementing memory allocation algorithms.
  Swapfile access: it controls the paging file access.
  Architecture-specific modules: they handle hardware-specific operations related to memory management (e.g. access to the MMU).
Architecture specific
modules
Memory Mapped Files
Swapfile Access
Core Memory Manager
Architecture-specific
modules
MMU
kswapd
System call interface
Notes: Regarding the architecture of the memory manager, it can be broken into smaller components or functionalities.
The first part of the memory manager is the system call interface, which provides memory manager services to the user space as previously seen.
The next part of the memory manager is memory-mapped files. This implements the functionality of memory file mapping algorithms.
The core memory manager is another part and is responsible for implementing memory allocation algorithms.
The memory manager also controls the paging file access through “Swapfile Access”.
Finally, architecture-specific modules are part of it. They handle hardware-specific operations related to memory management, for example, access to the MMU.

## Slide 20: Virtual File System
It is responsible for handling:
  Multiple hardware devices: it provides uniform access to hardware devices.
  Multiple logical file systems: it supports many different logical organizations of information on storage media.
  Multiple executable formats: it supports different executable file formats (e.g. a.out, ELF).
  Homogeneity: it presents a common interface to all of the logical file systems and all hardware devices.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The next component of the overall kernel, the virtual file system, is also responsible for handling a variety of tasks.
It provides uniform access to hardware devices and supports multiple logical file systems.
It also supports multiple executable file formats such as a.out and ELF.
Furthermore, it presents a common interface to all of the logical file systems and all the hardware devices.

## Slide 21: Virtual File System
It is responsible for handling:
  Performance: it provides high-speed access to files
  Safety: it enforces policies to not lose or corrupt data
  Security: it enforces policies to grant access to files only to allowed users, and it restricts user total file size with quotas.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: Another responsibility it has is to provide high-speed access to files to ensure high performance. It even enforces policies to not lose or corrupt data to ensure safety and integrity. Finally, it enforces policies to grant access to files only to allowed users and it restricts user total file size with quotas.

## Slide 22: Virtual File System
External interface:
  System-call interface based on normal operations on file from the POSIX standard (e.g. open/close/read/write)
  Intra-kernel interface based on i-node interface and file interface
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The external interfaces for the virtual file system are the system call interface and the intra-kernel interface. The system call interface is based on normal operations on files from the POSIX standard. These include open, close, read, and write. The intra-kernel interface is based on an i-node interface and a file interface.

## Slide 23: i-node
It stores all the information about a file excepts its name and the data it contains.
When a file is created, it is assigned a name and a unique i-node number (a unique integer number).
When a file is accessed
  Each file is associated with a unique i-node number.
  The i-node number is then used for accessing the data structure containing the information about the file being accessed.
struct inode {
struct hlist_node i_hash;
struct list_head i_list;
struct list_head i_sb_list;
struct list_head i_dentry;
unsigned long i_ino;
atomic_t i_count;
umode_t i_mode;
unsigned int i_nlink;
uid_t i_uid;
gid_t i_gid;
dev_t i_rdev;
loff_t i_size;
struct timespec i_atime;
struct timespec i_mtime;
struct timespec i_ctime;
...
Notes: An i-node is a data structure and it stores all the information about a file except its name and the data it contains.
When a file is created, it is assigned a name and unique i-node number.
When a file is accessed, the unique i-node number is used for accessing the data structure containing the information about the file that is being accessed.

## Slide 24: i-node Interface
create(): creates a file in a directory
lookup(): finds a file by name within a directory
link()/symlink()/unlink()/readlink()/follow_link(): manages file system links
mkdir()/rmdir(): creates or removes sub-directories
mknod(): creates a directory, special file, or regular file
readpage()/writepage(): reads or writes a page of physical memory
truncate(): sets the length of a file to zero
permission(): checks to see if a user process has permission to execute an operation
smap(): maps a logical file block to a physical device sector
bmap(): maps a logical file block to a physical device block
rename(): renames a file or directory
Notes: The i-node interface previously referenced provides a lot of functionality. This includes
  - “create”, which creates a file in a directory
  - “lookup”, which finds a file by name within a directory
  - “link”, “symlink”, “unlink”, “readlink”, or “follow link”, which manages file system links
  - “mkdir” or “rmdir”, which creates or removes a sub-directory
  - “mknod”, which creates a directory, special file, or regular file
  - “readpage” or “writepage”, which reads or writes a page of physical memory
  - “truncate”, which sets the length of a file to zero
  - “permission”, which checks to see if a user process has permission to execute an operation
  - “smap”, which maps a logical file block to a physical device sector
  - “bmap”, which maps a logical file block to a physical device block
  - “rename”, which renames a file or directory

## Slide 25: File Interface
open()/release(): opens or closes the file
read()/write(): reads or writes the file
select(): waits until the file is in a particular state (readable or writeable)
lseek(): moves to a particular offset in the file
mmap(): maps a region of the file onto the virtual memory of a user process
fsync()/fasync(): synchronizes any memory buffers with the physical device
readdir(): reads the files that are pointed to by a directory file
ioctl(): sets file attributes
check_media_change(): checks to see if a removable media has been removed
revalidate(): verifies that all cached information is valid
Notes: Then, there is the file interface, which was also mentioned. This, too, provides similar functionality, such as
  - “open” or “release”, which opens or closes the file
  - “read” or “write”, which reads or writes to the file
  - “select”, which waits until the file is in a particular state, such as readable or writeable
  - “lseek”, which moves to a particular offset in the file
  - “mmap”, which maps a region of the file into the virtual memory of a user process
  - “fsync” or “fasync”, which synchronizes any memory buffers with the physical device
  - “read dir”, which reads the files that are pointed to by a directory file
  - “i o control”, which sets file attributes
  - “check media change”, which checks to see if a removable media has been removed
  - “revalidate”, which verifies that all cached information is valid

## Slide 26: Virtual File System Architecture
System-Call interface
Logical file system
ext
ext2
fat
nfs
smbfs
proc
iofs
Binary Executable
ELF
a.out
script
Buffer cache
kflushd
buffer
Device drivers
char
block
Notes: Here is a diagram that displays the flow of the virtual file system architecture.

## Slide 27: Virtual File System Architecture
System call interface: it provides Virtual File System services to the user space
Logical file system: it provides a logical structure for the information stored in a storage medium.
  Several logical file systems are supported (e.g. ext2, fat).
  All files appear the same to the user.
  The i-node is used to hide logical file system details.
  For each file, the corresponding logical file system type is stored in the i-node.
  Depending on the information in the i-node, the proper operations are activated when reading/writing a file in a given logical file system.
Buffer cache: it provides data caching mechanisms to improve performance of storage media access operations.
Binary executable: it supports different types of executable files transparently to the user.
Notes: The architecture of the virtual file system provides virtual file system services to the user space, in the form of a system call interface. It also provides a logical structure for the information stored in a storage medium, in the form of a logical file system.
This supports several logical file system types, such as ext2 and fat. All of the files appear the same to the user and the i-node is used to hide logical file system details. For each file, the corresponding logical file system type is stored in the i-node. Depending on the information in the i-node, the proper operations are carried out when reading and writing to a file in a given logical file system.
The architecture also includes a buffer cache, providing data caching mechanisms to improve performance of storage media access operations.
Support for different types of executable files is also included.

## Slide 28: Virtual File System Architecture
Device drivers provide a uniform interface to access hardware devices:
  Character-based devices are hardware devices accessed sequentially (e.g. serial port).
  Block-based devices are devices that are accessed randomly and whose data is read/written in blocks (e.g. hard disk unit).
Device drivers use the file interface abstraction:
  Each device can be accessed as a file in the file system through a special file, the device file, associated with it.
  A new device driver is a new implementing of the hardware-specific code to customize the file interface abstraction (more about this later).
Notes: Device drivers are another important part and provide a uniform interface to access hardware devices. There are typically two types of devices: character-based and block-based. Character-based devices are hardware devices that are accessed sequentially, such as a serial port. A block-based device is accessed randomly, and data is read or written in block, for example, a hard-disk unit.
Device drivers use the file interface abstraction. Each device can be accessed as a file in the file system through a special file, known as the device file, that is associated with it. A new device driver is a new implementation of the hardware-specific code to customize the file interface abstraction.

## Slide 29: Inter-process Communication
It provides mechanisms to processes for allowing:
  Resource sharing
  Synchronization
  Data exchange
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: Another feature the kernel supports is IPC. This encompasses the ability to share resources, as well as synchronize and exchange data.

## Slide 30: Inter-process Communication Architecture
System call interface: it provides inter-process communication (IPC) services to the user space
The following IPCs are supported:
  Pipes
  Message queues
  Shared memory
  Semaphores
  Domain sockets
  Wait queues
  Signals
System-Call interface
File IPC
pipes
System V IPC
Message queue
Shared memory
Semaphores
Kernel IPC
Wait queue
Signal
Network IPC
Domain socket
Notes: The IPC service is provided to the user space as a system call interface. IPC can take many forms, as different processes may need to communicate via different methods. Some examples include pipes, message queues, shared memory, semaphores, domain sockets, wait queues, and signals. Looking at this diagram, we can see how each of these methods falls into different categories in regard to IPC and what they may be used for. For example, pipes are commonly used for IPC regarding files.

## Slide 31: Network
Provides support for network connectivity
  It implements network protocols (e.g. TCP/IP) through hardware-independent code.
  It implements network card drivers through hardware-specific code.
Inter-Process
Communication
Memory Manager
Hardware independent
Hardware dependent
Network
Network Protocols
Hardware driver
Virtual File System
Logical File System
Hardware Drivers
Process Scheduler
Hardware independent
Hardware dependent
Notes: The kernel also supports networking and provides support for network connectivity. In order to do this, it implements network protocols such as TCP and IP through hardware-independent code. It also implements the network card drivers; however, these are implemented with hardware-specific code.

## Slide 32: Summary
Linux architecture
Device trees
The U-BOOT bootloader
Notes: We will now take a look at device trees.

## Slide 33: Device Trees
To manage hardware resources, the Kernel must know which resources are available in the embedded system (i.e. the hardware description: I/O devices, memory, etc).
There are two ways to provide this information to the Kernel:
  Hardcode it into the Kernel binary code. Each modification to the hardware definition requires recompiling the source code.
  Provide it to the Kernel when the bootloader uses a binary file, the device tree blob.
A device tree blob (DTB) file is produced from a device tree source (DTS).
  A hardware definition can be changed more easily as only DTS recompilation is needed.
  Kernel recompilation is not needed upon changes to the hardware definition. This is a big time saver.
Notes: In order for the kernel to manage its hardware resource, it needs to know which resources are actually available to the embedded system, for example, looking back to the hardware description and things such as I/O devices and memory.
There are two ways for the kernel to retrieve this information. One is that the information can be hardcoded into the kernel binary code. However, this means that each modification to the hardware definition requires recompiling the source code. The other method is to provide the information to the kernel when the bootloader uses a binary file, which is the device tree blob (DTB).
A DTB file is produced from a device tree source (DTS). The definition of the hardware can be changed much more easily, as only the DTS requires recompilation. This saves a large amount of time.

## Slide 34: Device Trees
In Arm architecture, all device tree source files are now located in either arch/arm/boot/dts or arch/arm64/boot/dts.
  .dts files for board-level definitions
  .dtsi files for included files
A tool, the device tree compiler, compiles the source into a binary form: the device tree blob (DTB).
  The DTB is loaded by the bootloader and parsed by the kernel at boot time.
Device tree files are not monolithic. They can be split in several files, including each other.
.dtsi
.dtsi
.dtsi
.dts
Notes: In Arm architecture, the DTS files are typically located in arch/arm/boot/dts or arch/arm64/boot/dts.
The “.dts” files are for board-level definitions and the “.dtsi” files are for included files.
The device tree compiler is a tool that compiles the source into a binary form: the DTB. The DTB is then loaded by the bootloader and parsed by the kernel at boot time.
These device tree files are not monolithic, so they can be split into several files, including each other.

## Slide 35: Device Tree Syntax
/ {
node0: node@0 {
a-string-property = ”A string”;
a-string-list-property = “string ”, “string 2”;
a-byte-data-property = [0x12 0x23 0x45 0x56];
child-node@0 {
a-reference-to-something = <&node1>;
};
child-node@1 {
};
};
node1: node@1 {
an-empty-property;
a-cell-property = <1 2 3 4>;
child-node@0 {
};
};
};
Node label
Node name
Property name
Property value as string
Property value as sequence of bytes
Property value as sequence of 32-bit integers
Reference to another node
node@1
node@0
root
child-node@0
child-node@1
child-node@0
Representation of the device tree
Address of the node
Notes: This is the content of a device tree file, and each of the parts are labelled to described what they are for.

## Slide 36: Device Tree Content
Under the root of the device tree, we can find:
A cpus node, which sub nodes describe each CPU in the system
A memory node, which defines the location and size of the RAM
A chosen node, which is used to pass parameters to kernel (the kernel command line) at boot time
An aliases node, to define shortcuts to certain nodes
One or more nodes defining the buses in the SoC
One or mode nodes defining on-board devices
/ {
alias {};
cpus {};
apb@80000000 {
apbh@80000000 {
/* some devices */
};
apbx@80040000 {
/* some devices */
};
};
chosen {
bootargs = “root=/dev/nfs”;
};
};
Notes: Under the root of the device tree, we can find a number of nodes. One is the “cpu” node, which will have sub-nodes that describe each CPU in the system. It will also have a “memory” node, which will define the location and the size of the RAM.
Another node under the root of the device tree is a “chosen” node, which is used to pass parameters to the kernel at boot time.
An “alias” node is also present and defines shortcuts to other nodes.

## Slide 37: Device Tree Addressing
The following properties are used:
  reg = <address1 length1 […] >, which lists the address sets (each defined as starting address, length) assigned to the node
  #address-cells = <num of addresses>, which states the number of address sets for the node
  #size-cells=<num of size cells>, which states the number of size for each set
Note:
  Every node in the tree that represents a device is required to have the compatible property.
  compatible is the key Linux uses to decide which device driver to bind to a device.
/ {
cpus {
#address-cells = <1>;
#size-cells = <0>;
cpu@0 {
compatible = "arm,cortex-a9";
reg = <0>;
};
cpu@1 {
compatible = "arm,cortex-a9";
reg = <1>;
};
};
};
Notes: In terms of device tree addressing, the following properties are used:
  - The first, called “req”, is a list of the address sets assigned to the node.
  - The second, called “#address-cells”, states the number of address sets for the node.
  - The third, called “#size-cells”, states the size for each set.
  Every node in the tree that represents a device is required to have the compatible property. “compatible” is the key Linux uses to decide which device driver to bind to a device.

## Slide 38: Device Tree Addressing
CPU addressing
  Each CPU is associated with a unique ID only.
  #size-cells=<0>, always
Memory mapped devices
  Typically defined by one 32-bit based address, and one 32-bit length
  #address-cells=<1>
  #size-cells=<1>
cpus {
#address-cells = <1>;
#size-cells = <0>;
cpu@0 {
compatible = "arm,cortex-a9";
reg = <0>;
};
};
/{
#address-cells = <1>;
#size-cells = <1>;
gpio1: gpio@0209c000 {
compatible = "fsl,imx6sx-gpio",
"fsl,imx35-gpio";
reg = <0x0209c000 0x4000>;
};
};
Notes: For CPU addressing, each CPU is associated with a unique ID.
Memory-mapped devices are typically defined by one 32-bit based address and one 32-bit length.

## Slide 39: Device Tree Addressing
External bus with chip select line
  Typically, address-cells uses 2 cells for the address value: one for the chip select number and one for the offset from the base of the chip select.
  #address-cells=<2>
  The length field remains as a single cell.
  #size-cells=<1>
  The mapping between bus addressing and CPU addressing is defined by the ranges property.
external-bus {
#address-cells = <2>
#size-cells = <1>;
ranges = <0 0 0x10100000 0x10000
1 0 0x10160000 0x10000>;
ethernet@0,0 {
compatible = "smc,smc91c111";
reg = <0 0 0x1000>;
};
i2c@1,0 {
compatible = "acme,a1234-i2c-bus";
reg = <1 0 0x1000>;
#address-cells = <1>
#size-cells = <0>;
rtc@58 {
compatible = "maxim,ds1338";
reg = <58>;
};
};
};
Bus address
Corresponding CPU address and range
Notes: Typically, address cells use two cells for the address value: one for the chip select number and one for the offset from the base of the chip select.
The length field remains as a single cell.
The mapping between bus addressing and CPU addressing is defined by the “ranges” property.

## Slide 40: Summary
Linux architecture
Device trees
The U-BOOT bootloader
Notes: We will now look at the U-Boot bootloader.

## Slide 41: The U-Boot Bootloader
Very popular bootloader among embedded system developers
Historic perspective
Today, it is the de-facto standard among embedded systems.
Nov’02 Mar’03 Apr’03 Oct’03 Dec’03 Apr’04 May’04
PPC MIPS32 MIPS64 NIOS2 Coldfire Microblaze ARM
x86
Notes: The U-Boot bootloader is one of the most popular among embedded system developers.
Throughout the years, it has updated and been made available for a number of computer architectures, as shown on this timeline.
As it stands today, it is the de-facto standard among embedded systems.

## Slide 42: The U-Boot Bootloader
U-Boot architecture is made of two halves:
1st half
  Written mostly in Assembly code
  It runs from the CPU on-chip memory (e.g., on-chip static RAM).
  It initializes the CPU RAM memory controller and relocates itself in off-chip RAM Memory.
2nd half
  Written mostly in C code
  It implements a command-line human-machine interface with scripting capabilities.
  It initializes the minimum set of peripherals to load the device tree Blob, the Linux Kernel, and possibly, the Initial RAM disk to RAM Memory.
  It starts the execution of the Linux Kernel.
Notes: U-Boot is a first- and second-stage bootloader. The first half is written mostly in assembly code and runs from the CPU on-chip memory, for example, on-chip static RAM. It initializes the CPU RAM controller and relocates itself in off-chip RAM.
The second half is written primarily in C code and implements a command-line human-machine interface with scripting capabilities. It initializes the minimum set of peripherals to load the DTB, the Linux kernel, and possibly the initial RAM disk to RAM (memory). It also starts the execution of the Linux kernel.

## Slide 43: The U-Boot Bootloader
Processor-dependent files:
  Specific to the CPU that will run U-Boot (e.g. CPU 1, CPU 2, CPU n)
Board-dependent files:
  Specific for the boards hosting the above CPU, which may have different sets of I/O (.e.g, Board 1, hosting CPU 1, and I/O A versus Board 2, hosting CPU 1, and I/O B)
General-purpose files:
  Suitable for all the boards/CPUs
  Implement the human-machine interface and the scripting feature of U-Boot
CPU 1
CPU 2
CPU n
CPU 1 files
CPU 2 files
CPU n files
Board1
Board2
Board m
CPU 1
CPU 1
CPU 2
I/O A
I/O B
I/O C
Board 1 files
Board 2 files
Board m files
Human-machine Interface
U-Boot source code
Notes: There are different groups of files in regard to the bootloader. One group of files is those that are considered “processor-dependent” files. These are specific to the CPU that is going to be running U-Boot, for example, in this diagram, “CPU 1” to “CPU n”.
There are also board-dependent files. These are specific to the boards that are hosting the CPU, which may have different sets of I/O, for example, in this diagram, “Board 1” hosting “CPU 1” and “I/O A”, versus “Board 2” hosting “CPU 1” and “I/O B”.
Then finally, there are the general-purpose files. These are suitable for all of the boards or CPUs. They implement the human-machine interface and the scripting feature of U-Boot.